+5 Volt Voltage Regulator Circuit

Explanation:  A voltage regulator provides a constant dc output voltage that is nearly independent of the input voltage, output load current, and temperature.  The supply voltage to a voltage regulator must be 2 - 3 volts above the regulator rating. For example, a 78L05 must have at least 7 to 8 volts as a supply to work properly.  The 7800 series voltage regulators are integrated circuits (IC) that provide a positive voltage output. The 7900 series supplies a negative voltage output.

7800 Series Chart:

| 7800 Series Voltage Regulators |
| --- |
| Type Number | Output Voltage |
| 7833 | +3.3 V |
| 7805 | +5.0 V |
| 7806 | +6.0 V |
| 7808 | +8.0 V |
| 7809 | +9.0 V |
| 7810 | +10.0 V |
| 7812 | +12.0 V |
| 7815 | +15.0 V |
| 7818 | +18.0 V |
| 7820 | +20.0 V |
| 7824 | +24.0 V |
| http:/ cmd |  |

Related Web Sites:

http://www.afreeland.com/node/16

http://www.sparkfun.com/commerce/tutorial_info.php?tutorials_id=83&page=1

http://www.sparkfun.com/commerce/tutorial_info.php?tutorials_id=57&page=1

http://www.scienceprog.com/7805-voltage-regulator-for-your-design/