Cornerstone Electronics Technology and Robotics I Week 14

Parallel Circuits

- Administration:

  - Prayer

- Electricity and Electronics, Section 7.1, Parallel Circuits:

  - A parallel circuit is one that has more than one pathway for the electrons to flow.  Unlike series circuit, when you remove a resistor in a parallel circuit, electrons continue to flow.

  - Identifying parallel circuits:  Each example below is a circuit with two parallel paths; all of the circuit configurations are electrically equivalent to each other.

Circuit 1		        Circuit 2		 Circuit 3		 Circuit 4

  - Everyday examples of parallel circuits:

    - Electrical outlets in a home  See: http://sol.sci.uop.edu/~jfalward/seriesparallelcircuits/seriesparallelcircuits.html  (House wiring diagram)

    - Lights in a home

    - Electrical car functions, such as the radio, horn, starter, lights, etc.

  - Voltage in a Parallel Circuit:

    - If components are connected in parallel to the source, the voltage drop across each component is the same as the source voltage.

    - Mathematically:

VT = V1 = V2 = V3 = ….. = VN

Where:

VT = Total voltage applied to the series circuit

V1 = Voltage drop across R1

V2 = Voltage drop across R2

V3 = Voltage drop across R3

VN = Voltage drop across RN

N = The number of resistors in the parallel

For example, if N = 2, then the 2 resistor parallel circuit and voltmeter setup is as follows:

And the corresponding voltage drop equation is:

VT = V1 = V2

If N = 5, then the 5 resistor parallel circuit is:

And the corresponding voltage drop equation is:

VT = V1 = V2 = V3 = V4 = V5

    - In the two circuits below, the connections in Figure 1 and Figure 2 are electrically equivalent.

Figure 1				       Figure 2

    - Perform Parallel Circuits Lab 1 – Voltage Drop in a Parallel Circuit

  - Current in a Parallel Circuit:

    - Kirchhoff’s Current Law:  The sum of the currents into a junction is equal to the sum of the currents out of that junction.

    - Mathematically:

ITOTAL in = ITOTAL out

Where:

ITOTAL in = the sum of currents into a junction

ITOTAL out = the sum of currents out of a junction

For Example:

Figure 3

Iin(a) + Iin(b) = Iout(a) + Iout(b) + Iout(c)

Another way of expressing Kirchhoff’s Current Law (see Figure 4):

IT = I1 + I2 + I3 + …+ IN

Where:

IT = Total current into a parallel resistor circuit

I1 = Current through R1

I2 = Current through R2

I3 = Current through R3

IN = Current through RN

Figure 4

Draw a parallel resistor circuit where N = 4 and show the total current and the currents through each resistor.  Assume conventional current flow.

    - See applets:

      - http://www.falstad.com/circuit/e-ohms.html

      - http://media.pearsoncmg.com/bc/aw_young_physics_11/pt2a/Media/DCCircuits/1202DCParallel/Main.html (#3, junction law)

    - Parallel circuits act as current dividers.  See the two examples below.

Example 1			    		     Example 2

    - Perform Parallel Circuits Lab 2 – Kirchhoff’s Current Law

  - Resistance in Parallel Circuits:

    - When resistors are connected in parallel circuits, the total resistance is always less than the value of the smallest resistor.

    - Reciprocal Rule:

      - The reciprocal of a number is equal to 1 divided by that number, e.g., the reciprocal of 4 is ¼, and the reciprocal of 87 is 1/87.

      - The total resistance of a parallel circuit is:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+1/RN

Where RT is the total resistance and

N is the total number of resistors in parallel.

      - Proof:  Since IT = I1 + I2 + I3 + …+ IN:

And IT = VS/RT and I1 = VS/R1, I2 = VS/R2, etc., then:

VS/RT = VS/R1 + VS/R2 + VS/R3 +…..+ VS/RN

Now factor out VS by dividing both sides of the 	equation by VS and you arrive at:

1/RT = 1/R1 + 1/R2 + 1/R3 +…..+1/RN

      - Example:  Find the total resistance in Circuit 5:

Circuit 5

1/RT = 1/R1 + 1/R2 + 1/R3

1/RT = 1/470 + 1/1000 + 1/2200

1/RT = 0.0021 + 0.001 + 0.0004

1/RT = 0.0035

RT = 1/0.0035

RT = 286 

    - Special Case 1:  Two resistor parallel circuit: Since 1/RT = 1/R1 + 1/R2, then

RT = R1R2/R1+R2

    - Special Case 2:  Resistors of equal value:

RT = R/N

Where:

R = the value of each resistor (all being the same) 	 		N = the number of resistors

For Example:

RT = R/N

RT = 100/2

RT = 50 

How many 1 K resistors in parallel would you need to create 	a total resistance of 1 ohm?

    - In a parallel circuit, a resistor that is much smaller than the other resistors dominates.

    - Applet:  http://www.lon-capa.org/~mmp/kap20/RR506a.htm

    - Perform Parallel Circuits Lab 3 – Total Resistance in a Parallel Circuit

  - Power in a Parallel Circuit:

    - The total power is equal to the sum of all the power of each resistor in the parallel circuit.

PT = P1 + P2 + P3 +…….+PN

Where PT is the total power consumed in the circuit and

N is the total number of resistors in parallel.

    - Power is also equal to the source voltage times the total current.

PT = VT x IT

Where PT is the total power consumed in the circuit,

VT is the source voltage, and

IT is the total current

- Electricity and Electronics, Section 7.2, Applications and Troubleshooting Parallel Circuits:

  - Solving for Resistance, Voltage, and Current in a Parallel Resistor Circuits:

    - Four equations are used to solve parallel resistor circuits.  They are:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+1/RN

VT = V1 = V2 = V3 = ….. VN

IT = I1 + I2 + I3 + …+ IN

V = I x R

V = I x R can be applied to the total circuit (VT = IT x RT) and 				to individual resistors (V1 = I1 x R1).

    - A table will be used to help solve our circuits.  To begin, a table as shown in Table 1 corresponds to the circuit in Figure 5:

Figure 5

Table 1

    - Table 2 lists all of the unknowns that will be solved.

Table 2

    - Step 1:  Find V1, V2, and V3.

VT = V1 = V2 = V3 = 24 V

See Table 3:

Table 3

    - Step 2:  Find I1, I2, and I3.

V1 = I1 x R1, therefore,

I1 = V1 / R1

I1 = 24 V / 12 

I1 = 2 A

I2 = V2 / R2

I2 = 24 V / 8 

I2 = 3 A

I3 = V3 / R3

I3 = 24 V / 4 

I3 = 6 A

See Table 4:

Table 4

    - Step 3:  Find IT.

IT = I1 + I2 + I3

IT = 2 A + 3 A + 6 A

IT = 11 A

See Table 5:

Table 5

    - Step 5:  Find RT.

1/RT = 1/R1 + 1/R2 + 1/R3

1/RT = 1/12 + 1/8 + 1/4

1/RT = 0.083 + 0.125 + 0.25

1/RT = 0.458

RT = 1/0.458

RT = 2.18 

Or an alternate way:

VT = IT x RT, therefore,

RT = VT / IT

RT = 24 V / 11 A

RT = 2.18 

See Table 6:

Table 6

    - Since all of the resistances, voltages, and currents are solved in the present problem, the power can now be calculated.

  - Solving for Power in a Parallel Resistor Circuits:

    - Two equations are used to solve for power in a parallel resistor circuit.  They are:

PT = P1 + P2 + P3 + …. + PN

P = V x I

P = V x I can be applied to the total circuit (PT = VT x IT) and to 			individual resistors (P1 = V1 x I1).

    - A column for power will be added to the table already used to solve our circuit.  See Table 7.

Table 7

    - Step 5:  Solve for P1, P2, P3, and PT.

P1 = V1 x I1

P1 = 24 V x 2 A

P1 = 48 W

P2 = V2 x I2

P2 = 24 V x 3 A

P2 = 72 W

P3 = V3 x I3

P3 = 24 V x 6 A

P3 = 144 W

PT = P1 + P2 + P3

PT = 48 W + 72 W + 144 W

PT = 264 W

See Table 8:

Table 8

  - Example Problem 1:

    - In following example problems, insert the known values into the tables and solve for all of the unknowns for the corresponding circuits.

  - Remember:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+ 1/RN

VT = V1 = V2 = V3 = ….. VN

IT = I1 + I2 + I3 + …+ IN

V = I x R

P = V x I

  - Example Problem 2:

  - Example Problem 3:

  - Example Problem 4:

  - Example Problem 5:

  - Solve problems 1, 2, 4, and 7 in Student Activity Sheet 7-2.

- Related Web Sites:

  - http://www.physics247.com/solved_problems/basic_circuits.php

  - http://www.acs.ryerson.ca/~kantorek/EES512/tutor2.html

  - http://people.clarkson.edu/~svoboda/eta/designLab/ParallelRDesign.html

  - http://www.glenbrook.k12.il.us/gbssci/phys/Class/circuits/u9l4d.html

  - http://www.allaboutcircuits.com/vol_1/chpt_5/3.html

- Suggested Home-Study Student Activity Sheets 7.1 and 7.2

- Example Problem Solutions:

  - Example Problem 1:

  - Example Problem 2:

  - Example Problem 3:

  - Example Problem 4:

  - Example Problem 5:

Electronics Technology and Robotics I Week 14

Parallel Circuits Lab 1 – Voltage Drop in a Parallel Circuit

- Purpose:  The purpose of this lab is to experimentally verify that the voltage drops across parallel resistors are equal.

- Apparatus and Materials:

  - 1 – Solderless Breadboard with 9 V Power Supply

  - 1 – Digital Multimeter

  - 1 – 1 K Ohm Resistor

  - 2 – 2.2 K Ohm Resistors

  - 1 – 4.7 K Ohm Resistor

- Procedure:

  - Wire the following circuit

  - Measure and record VAE, VBF, VCG, and VDH.

- Results:

- Conclusions:

  - How do the voltage drops VAE, VBF, VCG, and VDH relate to each other?

Electronics Technology and Robotics I Week 14

Parallel Circuits Lab 2 – Kirchhoff’s Current Law

- Purpose:  The purpose of this lab is to experimentally verify Kirchhoff’s Current Law.

- Apparatus and Materials:

  - 1 – Solderless Breadboard with 9 V Power Supply

  - 4 – Digital Multimeters

  - 4 - Switches

  - 2 – 220 Ohm Resistors

  - 1 – 330 Ohm Resistor

  - 1 – 470 Ohm Resistor

- Procedure:

    - In the following circuit, simultaneously measure the current at points A, B, C, and D.  With all switches closed, see if IA = IB + IC + ID.  Record the results.  Measure and record the currents of the other combinations in the table using open and closed switches.

    - Verify Kirchhoff’s Current Law for each case.

Note how the current through R1 changes as resistors R2, R3, and R4 are added or removed from the circuit.

- Results:

- Conclusions:

  - Does the experiment verify Kirchhoff’s Current Law?  Explain.

Electronics Technology and Robotics I Week 14

Parallel Circuits Lab 3 – Total Resistance in a Parallel Circuit

- Purpose:  The purpose of this lab is to experimentally verify the reciprocal rule for total resistance of a parallel circuit.

- Apparatus and Materials:

  - 1 – Solderless Breadboard

  - 1 – Digital Multimeter

  - 1 – 100 Ohm Resistor

  - 1 – 220 Ohm Resistor

  - 1 – 1K Resistor

  - 3 – 1.5K Resistor

- Procedure:

  - Resistors in Parallel:

    - Wire the following circuit below then calculate and measure/record RT.

  - Two Parallel Resistors:

    - Wire the following circuit below then calculate and measure/record RT.

  - Equal Resistors:

    - Wire the following circuit below then calculate and measure/record RT.

- Results:

  - Resistors in Parallel:

  - Two Parallel Resistors:

  - Equal Resistors:

- Conclusions:  In each case, evaluate how well the RT calculated matched the RT measured.  Explain any discrepancies.

  - Resistors in Parallel:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+1/RN

  - Two Parallel Resistors:

RT = R1R2/R1+R2

  - Equal Resistors:

RT = R/N