Cornerstone Electronics Technology and Robotics I Week 15

Combination Circuits (Series-Parallel Circuits)

- Administration:

  - Prayer

  - Turn in quiz

- Electricity and Electronics, Chapter 8, Introduction:

  - In this lesson, we will learn to analyze circuits with resistors in both series and parallel together and compute the total resistance         (equivalent resistance) for those circuits.  From there, we can calculate the voltage drop and current for each resistor in the circuit.

  - Series-parallel circuits are also called combination circuits.

  - Examples:

Figure 1 – Examples of Combination Circuits

  - See applets:

    - http://www.falstad.com/circuit/e-resistors.html

    - http://webphysics.davidson.edu/physlet_resources/bu_semester2/c10_combo.html

  - Regardless of the complexity of a series-parallel circuit, it can be solved when broken down into steps of individual series and parallel circuits.

  - Review:

    - Four equations are used to solve series resistor circuits.  They are:

RT = R1 + R2 + R3 + … + RN

VT = V1 + V2 + V3 + …+ VN

IT = I1 = I2 = I3 =…IN

V = I x R

V = I x R can be applied to the total circuit (VT = IT x RT) and to 			individual resistors (V1 = I1 x R1).

See Lesson 13, Series Circuits for details.  Link:  http://cornerstonerobotics.org/curriculum/lessons_year1/ER%20Week13,%20Series%20Circuits.pdf

    - Four equations are used to solve parallel resistor circuits.  They are:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+1/RN

VT = V1 = V2 = V3 = ….. VN

IT = I1 + I2 + I3 + …+ IN

V = I x R

See Lesson 14, Parallel Circuits for details.  Link:  http://cornerstonerobotics.org/curriculum/lessons_year1/ER%20Week14,%20Parallel%20Circuits.pdf

  - Power in Combination Circuits: The total power in a combination circuit is equal to the sum of the individual powers.

  - The variables used in Ohm's Law equations must be common to the same two points in the circuit under consideration.  This rule cannot be overemphasized. This is especially important in series-parallel combination circuits where nearby components may have different values for both voltage drop and current.

- Electricity and Electronics, Section 8.1, Solving a Complex Circuit:

  - The goal of series-parallel resistor circuit analysis is to be able to determine all voltage drops, currents, and power dissipations in a circuit.

  - Contracting the Circuit: Finding the total resistance and total current:  In this section, you will combine series and parallel resistors in a step by step process until the entire circuit is reduced to one equivalent resistor.

    - Step 1:   Assess which resistors in a circuit are connected together in simple series or simple parallel.

    - Step 2:  Re-draw the circuit, replacing each of those series or parallel resistor combinations identified in step 1 with a single, equivalent-value resistor.

    - Step 3:  Repeat Steps 1 and 2 until the entire circuit is reduced to one equivalent resistor.

    - Step 4:  Find the total current for the circuit.

  - Expanding the Circuit:  In this section, you will proceed step-by-step from the simplified version of the circuit back to its original form, plugging in values of voltage and current where appropriate until all values of voltage and current are known.

    - Step 5:  Taking total voltage and total current values, go back to last step in the circuit reduction process and insert those values where applicable.

    - Step 6:  From known resistances, total voltage, and total current values from step 5, use Ohm's Law to calculate unknown values (voltage or current)

    - Step 7:  Repeat steps 5 and 6 until all values for voltage and current are known in the original circuit configuration. Essentially, you will proceed step-by-step from the simplified version of the circuit back to its original, complex form, plugging in values of voltage and current where appropriate until all values of voltage and current are known.

    - Step 8:  Calculate power dissipations from known voltage, current, and/or resistance values.

Figure 2 – Example of Contracting and Expanding a Combination Circuit

Example 1:  Parallel resistors R1 and R2 are in series with resistor R3. See Figure 3.

(Note:  In the following examples, when you encounter a 			resistor labeled R1,2, it is an equivalent resistor for resistors R1 		and R2. R1,2,3,4,5 is the equivalent resistor for resistors R1, R2, R3, 		R4, and R5.  Similarly, V4,5 is the voltage drop across the 			equivalent resistor R4,5.)

Figure 3

Solve for the all of the unknowns in Table 1.

Table 1

  - Contracting the Circuit: Finding the Total Resistance, RT  and Total Current, IT :

    - Step 1:   Assess which resistors in a circuit are connected together in simple series or simple parallel.  In our circuit, R1 and R2 are in a simple parallel configuration.

    - Step 2:  Re-draw the circuit, (Figure 4), replacing each of those series or parallel resistor combinations identified in Step 1 with a single, equivalent-value resistor.  In this circuit, R1 and R2 are replaced with R1,2.

Figure 4

R1,2 = R/N

R1,2 = 100 / 2

R1,2 = 50 

    - Step 3:  Repeat Steps 1 and 2 until the entire circuit is reduced to one equivalent resistor.  (Step 1) - R1,2 and R3 are in a simple series configuration.  (Step 2) - Re-draw the circuit, (Figure 5), with R1,2,3 replacing R1,2 and R3.  Enter RT, (R1,2,3), into the solution table (Table 2).

Figure 5

RT = R1,2,3

RT = R1,2 + R3

RT = 50 + 50 

RT = 100 

Table 2

    - Step 4:  Find the total current for the circuit.

IT = VT / RT

IT = 50 V / 100 

IT = 0.5 A

See Table 3:

Table 3

  - Expanding the Circuit:  Find all remaining values of voltage and current.

    - Step 5:  Taking total voltage and total current values, go back to last step in the circuit reduction process, (Figure 6), and insert those values where applicable.  We can now determine the current through each series resistor in the equivalent circuit in Figure 8.4.

Figure 6

IT = I1,2 = I3 = 0.5 A

Enter the value of I3 into the solution table (Table 4).

Table 4

- Step 6:  From known resistances, total voltage, and total current values from Step 5, use Ohm’s Law to calculate unknown values (voltage or current).  In our example, calculate the voltage drop V3 across the series resistor R3 and the voltage drop V1,2 across the parallel combination (equivalent resistor, R1,2).

Figure 7

V3 = I3 x R3

V3 = 0.5 A x 50 

V3 = 25 V

V1,2 = I1,2 x R1,2

V1,2 = 0.5 A x 50 

V1,2 = 25 V

Since R1 and R2 are parallel resistors, the voltage drops V1 and 			V2 are the same value and equal to V1,2.

V1 = V2 = V1,2 = 25 V

We can now enter V1, V2, and V3 into the solution table (Table 5).

Table 5

    - Step 7:  Repeat steps 5 and 6 until all values for voltage and current are known in the original circuit configuration. Essentially, you will proceed step-by-step from the simplified version of the circuit back into its original, complex form, plugging in values of voltage and current where appropriate until all values of voltage and current are known.  Here, calculate the current through each parallel resistor (R1 and R2) in the parallel resistor combination.  Use Ohm’s Law.

Figure 8

I1 = V1 / R1

I1 = 25 V / 100 

I1 = 0.25 A

I2 = V2 / R2

I2 = 25 V / 100 

I2 = 0.25 A

Enter I1 and I2 into the solution table (Table 6).

Table 6

    - Step 8:  Calculate power dissipations from known voltage, current, and/or resistance values.

P1 = V1 x I1

P1 = 25 V x 0.25 A

P1 = 6.25 W

P2 = V2 x I2

P2 = 25 V x 0.25 A

P2 = 6.25 W

P3 = V3 x I3

P3 = 25 V x 0.5 A

P3 = 12.5 W

PT = VT x IT

PT = 50 V x 0.5 A

PT = 25 W

The final solution table (Table 7):

Table 7

Summary of Values:

Figure 9

  - Example 2:  This combination circuit is a more complicated set of series and parallel resistors.  See Figure 10.

Figure 10

Solve for the all of the unknowns in Table 8.

Table 8

  - Contracting the Circuit: Finding the Total Resistance, RT  and Total Current, IT :

    - Step 1:   Assess which resistors in a circuit are connected together in simple series or simple parallel.  In this circuit, R2 and R3 are in simple series in a parallel branch.  Also, R4 and R5 are in simple parallel configuration.

    - Step 2:  Re-draw the circuit, (Figure 11), replacing each of those series or parallel resistor combinations identified in Step 1 with a single, equivalent-value resistor.

Figure 11

To determine the equivalent resistance R2,3, add the series 				resistors R2 and R3 together.

R2,3:

R2,3 = R2 + R3

R2,3 = 100  + 50 

R2,3 = 150 

Also determine the equivalent resistor R4,5 for the 					parallel resistors, R4 and R5, using the formula for parallel 				resistors of equal value.

R4,5:

R4,5 = R/N

R4,5 = 56 / 2

R4,5 = 28 

    - Step 3:  Repeat Steps 1 and 2 until the entire circuit is reduced to one equivalent resistor.  (Step 1) - R1 and R2,3 are in a simple parallel configuration.  R4,5 and R6 are in a simple series configuration. (Step 2) - Re-draw the circuit, (Figure 12), with R1,2,3 replacing R1 and R2,3 and R4,5,6 replacing R4,5 and R6.

Figure 12

Determine the equivalent resistor R1,2,3 for the parallel 				resistors, R1 and R2,3, using the formula for two parallel 				resistors.

R1,2,3:

R1,2,3 = R1 x R2,3 / R1 + R2,3

R1,2,3 = 100  x 150  / 100  + 150 

R1,2,3 = 15,000 2 / 250 									R1,2,3 = 60 

Determine the equivalent resistor R4,5,6 for the series resistors, R4,5 and R6, using the formula series resistor formula.

R4,5,6:

R4,5,6 = R4,5 + R6

R4,5,6 = 28 + 150 

R4,5,6 = 178 

    - Step 3 again:  Repeat Steps 1 and 2 until the entire circuit is reduced to one equivalent resistor.  (Step 1) - R1,2,3 and R4,5,6 are in a simple series configuration. (Step 2) - Re-draw the circuit, (Figure 13), with R1,2,3,4,5,6 replacing R1,2,3 and R4.5.6.

Figure 13

Determine the equivalent resistor R1,2,3,4,5,6 for the series 				resistors R1,2,3 and R4,5,6 using the formula series resistor 				formula.

R1,2,3,4,5,6 = R1,2,3 + R4,5,6

R1,2,3,4,5,6 = 60 + 178

R1,2,3,4,5,6 = 238 

R1,2,3,4,5,6 = RT

Enter RT, (R1,2,3,4,5,6), into the solution table (Table 9).

Table 9

    - Step 4:  Find the total current for the circuit.

IT = VT / RT

IT = 100 V / 238 

IT = 0.42 A

See Table 10:

Table 10

  - Expanding the Circuit:  Find all remaining values of voltage and current.

    - Step 5:  Taking total voltage and total current values, go back to last step in the circuit reduction process, (Figure 8.12), and insert those values where applicable.

Figure 14

Determine the current through each series resistor in the 				equivalent circuit in Figure 14.

IT = I1,2,3 = I4,5,6 = 0.42 A

Also, we can calculate the voltage drop V1,2,3 across  					resistor R1,2,3.

V1,2,3 = I1,2,3 x R1,2,3

V1,2,3 = 0.42 A x 60 

V1,2,3 = 25.2 V

- Step 6:  From known resistances and total voltage / total current values from Step 5, use Ohm’s Law to calculate unknown values (voltage or current).  See Figure 15.

Figure 15

R1 and R2,3:

Since R1 and R2,3 are parallel resistors, the voltage drops V1 				and V2,3 are the same value and equal to V1,2,3.

V1 = V2,3 = V1,2,3 = 25.2 V

Knowing V1 and R1, solve for I1:

I1 = V1 / R1

I1 = 25.2 V / 100 

I1 = 0.25 A

The current through R2,3 is the total current IT less I1.

I2,3 = IT - I1

I2,3 = 0.42 A – 0.252 A

I2,3 = 0.168 A

I2,3 could have been solved using Ohm’s Law, I2,3 = V2,3 / R2,3

R4,5 and R6:

R4,5 and R6 are in series so they have the same current 				through them as R4,5,6.

I4,5,6 = I4,5 = I6 = 0.42 A

Knowing I6 and R6, solve for V6:

V6 = I6 x R6

V6 = 0.42 A x 150 

V6 = 63 V

Knowing I4,5 and R4,5, solve for V4,5:

V4,5 = I4,5 x R4,5

V4,5 = 0.42 A x 28 

V4,5 = 11.8 V

Update the solutions table with the values of V1, I1, V6 and I6 				(Table 11).

Table 11

- Step 7:  Repeat steps 5 and 6 until all values for voltage and current are known in the original circuit configuration.

Figure 16

R2 and R3:

R2 and R3 are in series so they have the same current 				through them as R2,3.

I2,3 = I2 = I3 = 0.168 A

Knowing I2 and R2, solve for V2:

V2 = I2 x R2

V2 = 0.168 A x 100 

V2 = 16.8 V

Knowing I3 and R3, solve for V3:

V3 = I3 x R3

V3 = 0.168 A x 50 

V3 = 8.4 V

R4 and R5:

Since R4 and R5 are parallel resistors, the voltage drops V4 				and V5 are the same value and equal to V4,5.

V4 = V5 = V4,5 = 11.8 V

Knowing V4 and R4, solve for I4:

I4 = V4 / R4

I4 = 11.8 V / 56 

I4 = 0.21 A

Since R4 and R5 are equal,

I4 = I5

Record voltages and currents into the solution table 					(Table 12).

Table 12

    - Step 8:  Calculate power dissipations from known voltage, current, and/or resistance values.

P1 = V1 x I1

P1 = 25.2 V x 0.252 A

P1 = 6.3 W

P2 = V2 x I2

P2 = 16.8 V x 0.168 A

P2 = 2.8 W

P3 = V3 x I3

P3 = 8.4 V x 0.168 A

P3 = 1.4 W

P4 = V4 x I4

P4 = 11.8 V x 0.21 A

P4 = 2.5 W

P5 = V5 x I5

P5 = 11.8 V x 0.21 A

P5 = 2.5 W

P6 = V6 x I6

P6 = 63 V x 0.42 A

P6 = 26.5 W

PT = VT x IT

PT = 100 V x 0.42 A

PT = 42 W

Check power total:

PT = P1 + P2 + P3 + P4 + P5 + P6

PT = 6.3 W + 2.8 W + 1.4 W + 2.5 W + 2.5 W + 26.5 W

PT = 42.0 W

The final solution table (Table 13):

Table 13

Summary of Values:

Figure 17

  - Example Problem 1:

    - Solve for all of the unknowns in the following circuit.  Fill in each unknown in the table below the circuit.

  - Remember, to solve series circuit problems, you can use any or all of the following equations:

RT = R1 + R2 + R3 + … + RN

VT = V1 + V2 + V3 + …+ VN

IT = I1 = I2 = I3 =…IN

V = I x R

  - Remember, to solve parallel circuit problems, you can use any or all of the following equations:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+1/RN

VT = V1 = V2 = V3 = ….. VN

IT = I1 + I2 + I3 + …+ IN

V = I x R

  - Example Problem 2:

    - Fill in the known values then solve for all of the unknowns in the following circuit.

  - Remember, to solve series circuit problems, you can use any or all of the following equations:

RT = R1 + R2 + R3 + … + RN

VT = V1 + V2 + V3 + …+ VN

IT = I1 = I2 = I3 =…IN

V = I x R

  - Remember, to solve parallel circuit problems, you can use any or all of the following equations:

1/RT = 1/R1 + 1/R2 + 1/R3 +………..+1/RN

VT = V1 = V2 = V3 = ….. VN

IT = I1 + I2 + I3 + …+ IN

V = I x R

- You are given a black box with two terminals. The box is known to contain six 1-ohm resistors.  Using ohm-meter, you measure the resistance between the terminals to be the following:

      - 0.75 Ohms

      - 1.5 Ohms

      - 2.25 Ohms

      - 3 Ohms

      - 4.5 Ohms

      - 6 Ohms

Determine the configurations of the six resistors inside the box that create each resistance value.

- Example Problem Solutions:

  - Example Problem 1:

  - Example Problem 2: