Capacitor Codes

Cornerstone Electronics Technology and Robotics I

Ceramic Disk Capacitor Value and Tolerance Codes:

Example  224K:  22 x 104 pF = 220,000 pF = 220 nF = 0.22 F  +/- 10%.

Ceramic Disk Capacitor Temperature Code:  See Page 2

Film Capacitor Value Code:  See Page 3

Ceramic Disk Capacitor Temperature Code:

Example   X7P:  The letter X designates a low temperature of -550 C.  The digit 7 designates a high temperature of +1250 C.  The letter P specifies that the capacitance will vary +/- 10% over the temperature range of -550 C to +1250 C.

Film Capacitor Value and Tolerance Codes:

Example  473K:  47 x 103 pF = 47,000 pF = 47 nF = 0.047 F  +/- 10%.