Electronics and Robotics I Week 25

Resistive Sensors

- Administration:

  - Prayer

- PicBasic Pro Programs Used in This Lesson:

  - General PicBasic Pro Program Listing:  http://www.cornerstonerobotics.org/picbasic.php

  - Lab 1 adc1 as a .pdf file:  http://www.cornerstonerobotics.org/code/adc1.pdf

  - Lab 1 adc2 as a .pdf file:  http://www.cornerstonerobotics.org/code/adc2.pdf

  - Lab 1 adc3 as a .pdf file:  http://www.cornerstonerobotics.org/code/adc3.pdf

  - Lab 2 braitenberg1 as a .pdf file:  http://www.cornerstonerobotics.org/code/braitenberg1.pdf

  - Lab 3 bend_sensor1.pbp as a .pdf file:  http://www.cornerstonerobotics.org/code/bend_sensor1.pdf

- Resistive Sensors:

  - PicBasic Pro POT vs. ADCIN Commands:

    - Depending upon the circuit conditions, resistive sensors may be read using the POT or ADCIN commands.

    - POT Command:

      - Resistive device normally within the 5 – 50 K ohm range.

      - The POT command measures the time it takes to charge a capacitor in a resistor/capacitor series circuit.  Knowing the value of the capacitor and the charging time, the PIC converts the time value into an 8-bit resistance value of 0 - 255.

      - There is no voltage source when using the POT command therefore it does not measure a voltage drop.  See the schematic comparison below.

      - Restricted to an 8-bit variable, giving outputs from 0 – 255.

      - See the following website for further discussion:  http://books.google.com/books?id=XYwuCq5u2oEC&pg=PA189&lpg=PA189&dq=resistive+sensors+picbasic+pro&source=web&ots=d9Vra7g0Z2&sig=dZ5Ml3R4vSSOCE9aeaxEronc8gw

    - ADCIN Command:

      - ADCIN, which reads an A/D converter (analog to digital converter), measures a voltage drop across a resistor.

      - There is a voltage source when using the A/D command ADCIN.

      - Variables may be 8, 10, or 12-bit, generating outputs of 0 – 255, 0 – 1024, or 0 – 4096 respectfully.  The ADCIN command is more accurate than the POT command.

POT Uses No Voltage Source		ADCIN Has a Voltage Source, VIN

      - This lesson will focus on the ADCIN command.

  - Voltage Divider Review:

    - Voltage at Point A, VA:

      - Current through the series resistors:

VIN = I RTOTAL, since RTOTAL = R1 + R2,

VIN = I (R1 + R2)

Solving for I,

I = VIN / (R1 + R2)

      - VOUT:

VOUT = I R2, since the current, I, was solved above,

VOUT = [VIN / (R1 + R2)] x R2, and

VOUT = VIN x R2 / (R1 + R2)

      - Cases:

        - When R2 equals R1, then VA equals ½ VIN.

        - When R2 is smaller than R1, then VOUT will be closer to 0 volts or ground; conversely, when R2 is larger than R1, then VOUT will be closer to VIN.

      - In our application, VIN = +5V, so VOUT varies from near 0 V to near +5 V.

    - Perform Resistive Sensors LAB 1 – Reading a Potentiometer

  - Photoresistor Sensors (Cadmium Sulfide, CdS, Photo Sensor):

    - Cadmium sulfide changes in resistance when exposed to varying degrees of light.  The resistance of a CdS photoresistor or photocell decreases as it receives more light (an inverse relationship).

    - Photocells have a relatively slow response to changes in light. The characteristic blinking of overhead fluorescent lamps, which turn on and off at the 60 Hertz line frequency, is not detected by photocells.

    - Demonstrate 60 Hz frequency using a photocell and phototransistor circuits and a frequency counter and oscilloscope.  Video?

    - If a photoresistor is substituted for R2 in the voltage divider above and it is illuminated brightly, its resistance will be low and VA will be near 0V.

    - In contrast, if the same photoresistor is shielded from light, its resistance will be high and VA will be near +5V.

    - Photoresistors normally require shielding because they are sensitive to ambient or surrounding light.

    - Use the photoresistor as R2 in the voltage divider.  See below:

CdS Photocell in Voltage Divider

      - Use the following formula to calculate the value for R1:

R1 = SQRT(CdSDARK * CdSBRIGHT)

Where:

R1       =  Resistance of Resistor 1,

CdsDARK     = Resistance of the CdS photocell in the    darkest condition the photocell will operate,

CdSBRIGHT = Resistance of the CdS photocell in the brightest condition the photocell will operate

      - Source and derivation of the equation:  http://www.societyofrobots.com/schematics_photoresistor.shtml

    - Complete Resistive Sensors LAB 2 – CdS Photoresistors

  - Other Resistive Sensors:

    - Bend Sensors:

      - The resistance of the sensor increases in proportion to the degree of bending or flexing.  For the Jameco #150551, 0 degrees is about 10K ohms and 90 degrees is 30K – 40K ohms.

      - Perform Resistive Sensors Lab 3 – Bend Sensors

      - Source for bend sensors: http://www.robotshop.ca/home/products/robot-parts/sensors/stretch-bend-sensors/

Electronics and Robotics I Week 25

Resistive Sensors LAB 1 – Reading a Potentiometer

- Purpose:  The purpose of this lab is to teach the student how to wire a PIC18F88 for analog/digital conversion, to expose the student to the PicBasic Pro command ADCIN, and to introduce the linear slide sensor.

- Apparatus and Materials:

  - 1 – Breadboard with +5V supply or an Analog/Digital Trainer

  - 1 – PIC 16F88 Microcontroller

  - 1 –  10 K Tripot

  - 1 – Phidgets Slide Sensor, Product # RB-Phi-20 from:

http://www.robotshop.ca/home/products/robot-parts/sensors/linear-rotary-resistors/index.html

- Procedure:

  - Wire the circuit below.  Use a 10K tripot for R3.  Make sure to read the note in the schematic.

  - Program the PIC16F88 with adc1.pbp, adc2.pbp, and then adc3.pbp.  Adjust R3 and note the values on the LCD screen for each program.

  - Now substitute the slide sensor for the 10K tripot.  Note the changes in the LCD value as the linear position of the slide sensor moves.

Electronics and Robotics I Week 25

Resistive Sensors LAB 2 – CdS Photoresistors

- Purpose:  The purpose of this lab is to acquaint the student with the use of a CdS photocell as a resistive sensor.

- Apparatus and Materials:

  - 1 – Robotic Car Platform

  - 1 – PIC 16F88 – I/P Microcontroller

  - 1 – LCD Screen, Jameco #618003

  - 1 – 20 K Ohm  Potentiometer

  - 2 – CdS Photoresistors, Jameco #120299 (300K-Dark, 8K-Light)

  - 1 – 4.7K Resistor

  - 4 – 1K  Resistor, Includes R3 and R8

  - 2 – 2N2222A NPN Transistors

- Procedure:

  - Wire the following circuit.

  - Program the PIC16F88 with braitenberg1.pbp.

  - Adjust the CdS photocells for the car to be attracted to the light.  See:   http://www.youtube.com/watch?v=N_X4_VVxOrE

- Challenges:

  - Line-follower:  Mount CdS sensors on your robotic car for the car to follow a taped line.  See: http://www.youtube.com/watch?v=ut0iTLZykog

  - Light-Steering:  Use one photocell to activate steering or forward motion for the robotic car.  Use a second photocell to turn the robotic car off.  The car must begin in the starting box and come to a complete stop in the finish box.

  - CdS switch:  Wire a circuit and program a PIC16F88 to serve as a light activated switch which turns on and off an LED.

Electronics and Robotics I Week 25

Resistive Sensors LAB 3 – Bend Sensors

- Purpose:  The purpose of this lab is to acquaint the student with the function of a bend sensor.

- Apparatus and Materials:

    - 1 – Breadboard

    - 1 – PIC 16F88 Microcontroller

    - 1 – 4.7K Ohm Resistor

    - 1 – 22K Resistor

    - 1 – 20K Tripot

    - 1 – Bend Sensor, Jameco #150551

    - 1 – LCD Screen, Jameco # 618003

    - 1 – Futaba 3003 Hobby Servo

- Procedure:

  - Wire the circuit bend_sensor1.

  - Program the PIC16F88 with bend_sensor1.pbp

  - Bend flex sensor and note servo movement.

  - Review the derivation of the equation in the graph below.

Derivation of Formula Used in bend_sensor1.pbp