In-Circuit Serial Programming with PicBasic Pro

Cornerstone Electronics Technology and Robotics II

- Administration:

  - Prayer

- In-Circuit Serial Programming (ICSP):

  - Up to this point, when programming a PIC chip, the chip was physically removed from the circuit and placed in the ZIF.  By using in-circuit serial programming, the PIC chip remains in the circuit while programming occurs.

  - Schematic for PIC16F88:

  - Photos:

Underside 10-Pin	          Top View 10-Pin Header Cable

Header Cable			    in melabs Programmer

Breadboard Connections

  - Schematic for PIC16F877A:

Electronics and Robotics II

In-Circuit Serial Programming LAB 1 – blink2

- Purpose:  The purpose of this lab is to acquaint the student with the ease of programming a PIC with in-circuit serial programming.

- Apparatus and Materials:

  - 1 – Analog/Digital Trainer or breadboard with 5 V Supply

  - 1 – 150 Ohm, ½ Watt Resistors

  - 1 – 4.7K, ½ Watt Resistor

  - 1 – LED

- Procedure:

  - Keep the ICSP connections to the breadboard

  - Open blink2.pbp and download to your chip.  Wire your breadboard for blink2.

- Change the pin location and blinking times and download without removing the PIC MCU.